Crime Prevention Through Environmental Design (C.P.T.E.D.) 			Test

Name: __________________________________________	Date: _________________

Circle the letter beside the most correct answer.

- Most home builders buy and install locks in new homes based primarily on:

  - lock quality

  - price

  - appearance

  - coordination with other décor of the home

- A single-cylinder deadbolt lock should not be used if it is within _______ inches of a window?

  - 56

  - 48

  - 40

  - 36

- The weakest part of an entry door assembly is generally considered to be?

  - the strike

  - the door knob

  - the hinges

  - the frame

- Which of the following items would NOT be considered a space or motion sensing device for an intrusion alarm system?

  - photo electric cell

  - ultrasound / microwave

  - passive infrared

  - floor pressure mat

- In general, the most expensive item in retrofitting an existing building for a camera system is the?

  - wiring

  - cameras themselves

  - data recorders

  - interface with the alarm system

- “A critical, on-site examination of a facility … to identify deficiencies and excesses” is a partial definition of?

  - CPTED

  - crime prevention

  - security assessment

  - victimization survey

- Which of the following would be considered a psychological barrier?

  - cyclone fence

  - a motion sensing gate

  - a see through glass door

  - a “no trespassing” sign

- In conducting a security assessment of an apartment complex, which of the following items is NOT a consideration?

  - obtain recent crime statistics

  - study demographic data

  - interview owners and users of the property

  - all are considerations to consider

- Colors can influence a person’s behavior. Which of the following is a behavioral influence that the color green would have?

  - sensation of brightness

  - calming effect on the nervous system

  - be an appetite stimulant

  - can cause eye irritation if too prominent

- “Deter’ is one of the four basic principles of CPTED. List the other three:

_________________, _______________, _________________

- “Natural Access Control” is one of the four basic concepts of CPTED. List the other three:

___________________________________________

___________________________________________

___________________________________________

- “The proper design and effective use of the built environment can lead to a reduction in crime and the fear of crime and lead to an improvement in the quality of life.” This is a definition of:

  - CPTED

  - crime prevention

  - security survey

  - victimization survey

- The proper application of CPTED principles attempts to control the environment of the:

  - criminal

  - potential victim

  - actual victim

  - abnormal user

- The focus of crime prevention centers around the three part of the crime triangle. Those three parts are desire, ability and _______________.

- One of the most difficult concepts of security is?

  - cost effectiveness

  - maintenance

  - natural access control

  - natural surveillance

- Which of the following statements is TRUE?

Territorial reinforcement  _______________

  - eliminates physical aspects of ownership, such as fences

  - encourages intruders

  - makes legitimate users feel safer

  - is often costly and difficult to achieve

- The largest percentage (up to 90%) of mistakes related to the basic CPTED principles of “proper design and effective use” of space occurs in which phase?

  - designation – for what purpose was the space intended to be used

  - design – how well does the physical design support the intended function

  - definition – is ownership of the space clearly defined

  - determination – does the use assessment support the design

- CPTED principles generally list three lines of defense for buildings. The first line of defense is the buildings perimeter. Name the other two.

_______________________________  ____________________________

- The minimum recommended height for a security fence is:

  - 6 feet

  - 8 feet

  - 10 feet

  - 12 feet

- For a four foot fence, the recommended depth for the post holes is 24 inches. For each additional foot in height, how many inches of post hole depth are recommended?

  - 3 inches

  - 4 inches

  - 6 inches

  - 8 inches

- If a person has a security fence around their property, what is the minimum amount of cleared space you would recommend on either side of the fence?

  - 10 feet

  - 15 feet

  - 20 feet

  - 25 feet

- A person has a hedge along the front wall of their home. How far below the window ledges would you recommend that they keep this hedge trimmed?

  - 3 inches

  - 6 inches

  - 9 inches

  - 12 inches

- A type of exterior lighting that gives off a yellow tint and results if poor color rendition of objects it illuminates is which of the following light sources?

  - incandescent

  - low pressure sodium

  - high pressure sodium

  - mercury vapor

- Which of the following types of lighting would you never recommend for security lighting?

  - pole mounted

  - wall mounted

  - roof mounted

  - ground mounted

- Exterior openings into buildings below a certain height are generally considered a cause for a security concern. What is this height?

  - 15 feet

  - 18 feet

  - 21 feet

  - 25 feet

- The minimum length of throw (extension) for a deadbolt lock is?

  - 5/8 of an inch

  - ¾ of an inch

  - 1 inch

  - 1 ¼ inches

- Most fire and life safety codes require that exterior doors on schools and commercial buildings open outward. This usually places the hinge pin on the outside of the building. Give one recommendation you would make to an owner of an existing building which this situation with regard to securing the pin.

__________________________________________________________

- Which of the following types of doors would you never recommend as an exterior door?

  - fiberglass

  - aluminum

  - wooden hollow core

  - polycarbonate

- What is the “3 – 7 rule” in CPTED?

___________________________________________________________

- There are two basic methods of slowing (calming) traffic. One attempts to control the volume of traffic. The other attempts to control the ________ of traffic.

  - type

  - speed

  - maneuverability

  - range

- To meet the requirements for a Homeowners Insurance Safety Inspection all windows must have what type of lock.

  - Thumb screw

  - Key operated

  - Primary lock

  - Secondary lock

- Windows in which both sashes moves (opens) within the frame is known as a ___________

  - single hung

  - casement

  - hopper

  - double hung

- Polycarbonate is about _________ times stronger than plate glass.

  - 50

  - 150

  - 300

  - 450

34.) BONUS QUESTION – WORTH FIVE POINTS    Name the person who coined the term CPTED.