UL Record Safe Classifications

Classification 	Temperature		Time		Impact	Old Label

350-4			2,000°F	`	4hr		Yes		      A

350-2			1,850°F		2hr.		Yes		      B

350-1			1,700°F		1hr.		Yes		      C

350-1 (Insulated Filing Device)	1,700°F		1hr.		No		      D

UL Computer Media Storage Classifications

150-4			2,000°F		4hr.		Yes

150-2			1,850°F		2 hr.		Yes

150-1			1,700°F		1hr.		Yes

Look for Classification Marking on Product

Insulated Record Containers Class 125

Classified by:

Underwriter Laboratories, Inc.

As to Fire Resistance Only

Rating: Class 125-2

UL Money Safe Classifications

Adapted from Handbook of Loss Prevention and Crime Prevention, Third Edition, by Lawrence   J. Fennelly

Label		Description				Construction

TL15		Tool resistant			Weight: at least 750 lb. or anchored

Body: At least 1 inch thick steel or equal.

Attack: Door and front face must resist attack with common hand and electric tools for 15 minutes.

TL30		Tool resistant			Weight: At least 750 lb. or anchored.

Body: At least 1 inch thick steel or equal

Attack: Door and front face must resist attack with common hand and electric tools plus abrasive cutting wheels and power saws for 30 minutes

TR30* 	Tool or Torch			Weight: At least 750 lb.

(No longer           Resistant                                  Attack: Door and front face must resist attack with tools

manufactured)                                                               listed and oxy-fuel gas cutting or welding torches for 30 minutes.

TRTL30X6	Tool or Torch			Weight: At least 750 lb.

Resistant	Attack: Door and entire body must resist attack with tools and torches listed plus electric impact hammers for 30 minutes.

TXTL60	Tool, Torch&			Weight: At least 1,000 lb.

Explosive Resistant	Attack: Door and entire safe body must resist attack with tools and torches listed plus 8 ounces of nitroglycerin or equal for 60 minutes.